## Slide 1: Maritime resource names (MRN) it’s value and use
Minsu Jeon, Technical Operations Manager

## Slide 2: Contents
    Unique identifier
    Technical aspects
      URI, URL, URN
      Example
    MRN
    Value and potential uses
    MRN registry
    Procedure
    Way forward

## Slide 3: Unique identifier for all types of resources
Maritime Resources
AtoN
Equipment
AIS
e-Navigation
Publications
Nautical Charts
IMO number
Container ID
Navigation Aids
MMSI
VTS
Lights
Buoys
Organizations
People
Electronic services
Message ID
Berth No.
Communication channel ID

## Slide 4: What is Maritime Resource Names (MRN) ?
MRN is a naming scheme that can uniquely identify any maritime resource on a global scale. This could be organization, employees, a person, a physical or a virtual object, for instance, an electronic document, a buoy, a ship, a mariner, a nautical chart or an electrical service.
MRN will be an essential method to identify all maritime resource machine readable in the e-Navigation environment.

## Slide 5: URI, URL, URN
URI (Uniform Resource Identifier)
<Scheme>:<Scheme-specific-structure>
URN (Uniform Resource Names)
Paul Petry
urn:mrn:iala:person:nnnn.n
What
URL(Uniform Resource Locator)
10 rue des Gaudines 78100
Saint Germain en Laye
http://iala-aism.org/
Where

## Slide 6: Example of URN
URN | corresponds to
urn:isbn:0451450523 | The 1968 book The Last Unicorn, identified by its book number.
urn:isan:0000-0000-9E59-0000-O-0000-0000-2 | The 2002 film Spider-Man, identified by its audiovisual number.
urn:ISSN:0167-6423 | The scientific journal Science of Computer Programming, identified by its serial number.
urn:ietf:rfc:2648 | The IETF's RFC 2648.
urn:mpeg:mpeg7:schema:2001 | The default namespace rules for MPEG-7 video metadata.
urn:oid:2.16.840 | The OID for the United States.
urn:nbn:de:bvb:19-146642 | A National Bibliography Number for a document, indicating country (de), regional network (bvb = Bibliotheksverbund Bayern), library number (19) and document number.
urn:lex:eu:council:directive:2010-03-09;2010-19-UE | A directive of the European Union, using the proposed Lex URN namespace.
urn:lsid:zoobank.org:pub:CDC8D258-8F57-41DC-B560-247E17D3DC8C | A directive of the Life Science Identifiers may be resolved to http://zoobank.org/urn:lsid:zoobank.org:pub:CDC8D258-8F57-41DC-B560-247E17D3DC8C .
urn:uuid:6e8bc430-9c3a-11d9-9669-0800200c9a66 | A version 1 UUID.
Source: Wikipedia

## Slide 7: Maritime Resource
Maritime
Resource
should have an unique identifier
so that people and systems could distinguish it from any other resources
should be addressable
should have a rough location to be capable of being manipulated using a syntax

## Slide 8: Requirements for MRN
Unique. Every id that is created must differ from any other id that is created.
Decentralized. It must be possible to create IDs without relying on a single global source that must be used every time an ID is created.
Forward compatible. It must be possible to add new naming schemes for new maritime domains in the future. Technologies will only come and go with an ever-increasing rate in the coming years.
Flexible. The naming scheme must be very flexible and allow for identifying any type of resource such as documents, cargo, routes, equipment, ships and mariners, giving no preference to any specific type of IDs.

## Slide 9: MRN syntax
The basic syntax for a MRN is defined using the Augmented Backus-Naur Form (ABNF) as specified in [RFC5234]: <MRN> ::= "urn" ":" "mrn" ":" <OID> ":" <OSS> [ rq-components ] [ "#" f-component ] <OID> ::= (alphanum) 0*20(alphanum / "-") (alphanum) ; Organization ID <OSS> ::= <OSNID> ":" <OSNS> ; Organization-specific string <OSNID> ::= (alphanum) 0*32(alphanum / "-") (alphanum) ; Organization-specific namespace ID <OSNS> ::= pchar *(pchar / "/") ; Organization-specific namespace string
DIGIT ::= %x30-39 ; 0-9
ALPHA ::= %x61-7A ; a-z
The entire MRN is case-insensitive.
URN:OID:OSS:OSNID:OSNS

## Slide 10: MRN

## Slide 11: Use of MRN
Communication
- AtoN authorities
- Hydrographic offices
- Military
- Meteorology service
- Port service
- University
- etc.
Maintenance
- AtoN monitoring
- Inventory management
- etc.
Information exchange
- VTS services
- S100/200
- MSI
- etc.
E-Navigation services

## Slide 12: MRN structure(Example)
URN
MRN
Remain fixed
:Resource
owner
:Resource instance
:Resource type
:Resource sub type
Collected and shared
Matter for the resource owner
BIMCO
IMO
IHO
IALA
Publication
Feature types
IMO number
CIRM
IEC
ITU
MMSI
Member
nnnn.n
Country A
Nautical charts
Buoys
Lighthouses
nnnn.n
AtoN
Hydrography
Equipment
Notice to mariners
Coastguard
Weather infor
nnnn.n
nnnn.n
nnnn.n
nnnn.n
Country B
Lighthouses
nnnn.n
AtoN
…..…

## Slide 13: MRN registry
Country A
Data collection
List of lights
MSI
Risk Assessment
e-Navigation
Big data analysis
Information
Service
MRN Database
IHO
IMO
CIRM
BIMCO
WMO
Country B
Country C

## Slide 14: Procedure on obtaining the MRN
Representative of recognized organization
Organization ID
IALA secretariat
mrn@iala-aism.org
Template
IALA Domain Administrator will:
Validate the request of the recognized organization;
Update the organization ID
Inform the organization of the decision
When there is an appeal:
Forward the appeal to IALA DSG for final decision;
Inform the appellant of the decision
Arrange of MRN

## Slide 15: Way forward
Discuss about MRN concept
The google group: https://groups.google.com/forum/#!forum/mrn-discuss
Join IALA Technical committee to develop a guidance

## Slide 16: Questions?