## Slide 1: Perception of Flashing Lights
28/09/10
EEP15 WG4
Ian Tutt
General Lighthouse Authorities R&RNAV Directorate
Harwich
Essex
UK
EEP16/INF/4
Notes: <number>

## Slide 2: Introduction
28/09/10
EEP15 WG4
Luminous Range
Observer Illuminance
Effective Intensity
Apparent Intensity
What’s the difference?
Way Forward
Notes: <number>

## Slide 3: Luminous Range
28/09/10
EEP15 WG4
Luminous Range is a calculated figure based on:
  Light Intensity
  Illuminance at the observer
  Atmospheric transmissivity
From Allard:
where: E = illuminance
T = transmissivity
I = intensity
d = distance
d is range when E(d) is at the threshold of perception
Notes: <number>

## Slide 4: Threshold Illuminance
28/09/10
EEP15 WG4
From the International Lighting Vocabulary:
“Threshold of illuminance: smallest illuminance produced at the eye of an observer by a light source seen in point vision, which renders the source perceptible.
Note: For visual signalling, the light source must be rendered recognisable, and hence a higher threshold of illuminance is to be expected.”
Notes: <number>

## Slide 5: Observer Illuminance
28/09/10
EEP15 WG4
In 1933 an international lighthouse conference in Paris recommended that the minimum illuminance at the observer required to safely recognise an aid to navigation signal light was 0.67 sea-mile candelas (0.2 microlux)
Since then, all luminous range calculations for maritime AtoN use have been based on that illuminance figure.
Therefore d is the luminous range when E(d) in the Allard equation is 0.2 microlux.
Notes: <number>

## Slide 6: Effective Intensity
28/09/10
EEP15 WG4
Effective intensity is defined as the luminous intensity of a steady light source that would have the same luminous range as the flashing light in question.
Luminous range for marine AtoN signal lights is based on an observer illuminance of 0.2 microlux.
However, most experiments that investigated effective intensity were based on an observer’s detection of a light at achromatic threshold of illuminance - where the observer could just detect the light (approx 0.05microlux).
Notes: <number>

## Slide 7: Effective Intensity
28/09/10
EEP15 WG4
For a rectangular flash, the Blondel-Rey equation for effective intensity is valid:
    where: Ie = effective intensity
    Io = peak intensity
    t = flash duration
    a = the visual time-constant
    the value of a is typically 0.2 for nighttime use
This equation holds true for flashing lights at the achromatic threshold of perception (Et).
Notes: <number>

## Slide 8: Toulmin-Smith and Green
28/09/10
EEP15 WG4
At the 1933 conference in Paris, one of the papers presented was an experiment by Toulmin-Smith and Green of UK.
Their experiment investigated the perception of flashing lights at illuminances above threshold (supra-threshold) – the flash profiles were rectangular.
They used ‘brightness matching’ to plot curves of visual perception at Et (threshold) and several illuminance values of Ec (supra-threshold).
Notes: <number>

## Slide 9: Toulmin-Smith and Green
28/09/10
EEP15 WG4
Extract from Toulmin-Smith and Green’s paper of 1933.
Notes: <number>

## Slide 10: Apparent Intensity
28/09/10
EEP15 WG4
As the definition of effective intensity only provides for flashing lights at threshold (Et), we need another term to explain the perception of flashing lights above threshold at different illuminance levels (Ec).
It is proposed that the deprecated term “apparent intensity” (Ia) is revived and used for this purpose.
Because the perception of a flash changes with the level of illuminance, it is proposed that a level of illuminance in microlux is stated with the apparent intensity (Ia, Ec).
Notes: <number>

## Slide 11: Variable a Approach
28/09/10
EEP15 WG4
It has been suggested that apparent intensity can be modelled by varying the value of the Blondel-Rey visual time-constant a and linking it to the value of illuminance.
In 1933, Hampton suggested using a formula for such a purpose:
This formula can be used to calculate a value for a in the Blondel-Rey equation for different illuminance levels.
Notes: <number>

## Slide 12: Variable a Approach
28/09/10
EEP15 WG4
Notes: <number>

## Slide 13: What’s the Difference?
28/09/10
EEP15 WG4
Flash Duration (s) | Effective Intensity Ie | Apparent Intensity Ia (at 0.2 μlux) | % Increase
0.05 | 19 | 35 | 85%
0.1 | 32 | 54 | 66%
0.15 | 42 | 63 | 51%
0.2 | 49 | 69 | 41%
0.25 | 55 | 74 | 36%
0.3 | 59 | 78 | 32%
0.4 | 66 | 85 | 30%
0.5 | 70 | 90 | 29%
Notes: <number>

## Slide 14: Way Forward
28/09/10
EEP15 WG4
Repeat T-S & G’s experiment (rectangular flashes)
Test for non-rectangular flashes
Test with background luminance
Test for different colours
Test for different colours of light against different background colours
Find most appropriate model at each stage
Notes: <number>

## Slide 15: Thank You
28/09/10
EEP15 WG4
ian.tutt@gla-rrnav.org
Ian Tutt
General Lighthouse Authorities R&RNAV Directorate
Harwich
Essex
UK
Notes: <number>